## Slide 1: MUL Improvement: Karatsuba Algorithm
Let X = Xl * 2n/2 + Xr and Y = Yl * 2n/2 + Yr,
Where Xl and Yl are the leftmost n/2 bits and Xr and Yr are the rightmost n/2 bits of X and Y respectively
Thus, the multiplication of X and Y can be represented as
XY = (Xl * 2n/2 + Xr)(Yl * 2n/2 + Yr)
= 2n XlYl + 2n/2(XlYr + XrYl) + XrYr
Here, XlYr + XrYl can also be written as
XlYr + XrYl = (Xl + Xr)(Yl + Yr) – XlYl – XrYr
So, XY will be
XY = 2n XlYl + 2n/2((Xl + Xr)(Yl + Yr) – XlYl – XrYr) + XrYr

## Slide 2: XY = 2n XlYl + 2n/2((Xl + Xr)(Yl + Yr) – XlYl – XrYr) + XrYr
There are 3 main multiplication needed to get the result:
XlYl
XrYr
(Xl + Xr)(Yl + Yr)
All of these can be calculated independently once X and Y are known, getting the result for the first and last 1/3 part, and the partial result for the middle 1/3.
After getting all 3, calculate the middle 1/3 and do appropriate shifting and addition to get the final result

## Slide 3
A B
C D
AD BD
AC BC
+
Total multiplication: 4
Karatsuba Algorithm
AC
BD
(A+B)(C+D)
Total multiplication: 3
Example 2-bit MUL:
Similar for 32-bit MUL:
Total multiplication: 32 x 32 = 1024
Total multiplication: 16 x 16 x 3 = 768
3 part of the multiplication
16-bit multiplication
32-bit multiplication

## Slide 4: A FSM Hazard Detection Unit (Mealy Machine)
IDLE
STALL
LOAD
1
STALL
LOAD
STALL
LOAD
2
CLEARSTALL
FSM will stay in IDLE STATE if no hazard or control hazard, in control hazard it will flush the register walls
FSM will enter STALL_LOAD state when encounter load-use hazard, and then enter clear state, stalling processor for 2 cycles
FSM will enter STALL_LOAD_1 state when encounter store-load hazard, and then enter STALL_LOAD_2 state, finally clear state, stalling processor for 3 cycles

## Slide 5: 2-bit Dynamic Branch Predictor
Reduces the wasted cycles from always 2 to now potentially 0 for conditional branches
Starts here